## Slide 1
Voice-to-Text for OpenEMR
CSC 436 · Spring 2026 · University of Arizona
Andy Siegel · Fig Lesser · Kianny Calvo · Tokhirjon Vokhidov
Team 1

## Slide 2
The Problem
Clinicians spend 30–50 % of their workday on EHR documentation
• OpenEMR — a widely-used open-source EHR — has no native voice input
• Typing notes during a patient encounter breaks eye contact and disrupts the visit
• Documentation overload is a leading driver of physician burnout
• Existing commercial voice tools are expensive, cloud-dependent, or not integrated with OpenEMR
"The most time-consuming part of the encounter workflow is dictating the chief complaint." — Nirav Merchant, Co-PI NSF CyVerse (stakeholder interview)

## Slide 3
The Solution
🎙 Speak
Clinician speaks during the encounter
⚡ Transcribe
Whisper runs locally — no cloud
🧠 Extract
spaCy NLP identifies clinical entities
✅ Confirm
Clinician reviews & approves
📋 Insert
Text injected into OpenEMR form
›
›
›
›
• Chrome extension — attaches to the OpenEMR encounter page, no source-code changes required
• All processing is local — no audio or patient data ever leaves the machine (HIPAA-aligned)
• Confirm-before-fill safeguard — clinician reviews the transcript before anything is written to the EHR
• Dual NLP: fast spaCy rule-based path + optional local Ollama LLM for conversational phrasing

## Slide 4
Project Goal & Success Criteria
Word Error Rate (WER)
< 10 % on a standardized clinical speech test set
Measured against publicly available medical ASR benchmarks (MedASR, MedWhisper)
Medical Terminology Accuracy
> 90 % on drug names, diagnoses, procedures
Evaluated against curated set from UMLS clinical terminology sources
Transcription Latency
≤ 2 seconds from end of utterance to text display
Timed end-to-end: stop button → text appears in preview panel
Offline Operation
Within 5 % of online accuracy and latency baseline
System runs fully without internet; comparison measured in controlled setting

## Slide 5
Project Users
Who Uses This?
• Primary care physicians
• Urgent care clinicians
• Outpatient specialists
• Any provider using OpenEMR for encounter documentation
Why?
• Reduce documentation time — speak instead of type
• Keep attention on the patient during the encounter
• Lower risk of burnout from after-hours charting
Stakeholder
Nirav Merchant
Co-PI, NSF CyVerse
✓ Validated 'Reason for Visit' as the highest-priority insertion target
✓ Confirmed: dictating the chief complaint is the most time-consuming step
✓ Requested confirm-before-fill to prevent accidental EHR writes
✓ Positively called out the safety dialog in follow-up feedback

## Slide 6
What's Novel?
Existing Option
Problem
Nuance Dragon Medical
$$$, cloud-required, not OpenEMR-integrated
Google/Browser Speech API
No medical accuracy, sends PHI to the cloud
EHR-vendor voice tools
Tied to expensive proprietary EHR platforms
Generic open-source STT
No clinical NLP, no OpenEMR integration
Our Approach
✓ Free & open-source — zero licensing cost
✓ Fully offline — no PHI leaves the machine
✓ Browser extension — no OpenEMR source changes, survives EHR updates
✓ Medical-domain NLP — chief complaint, assessment, plan, meds, diagnoses
✓ Dual NLP engine — fast spaCy + local Ollama LLM with graceful fallback
✓ Confirm-before-fill — patient safety built into the UX
There is no existing free, offline, OpenEMR-native voice-to-text tool with medical-domain NLP.

## Slide 7
System Architecture
Chrome Extension (Manifest V3)
content.js · scanner.js Floating panel UI Field detection & injection
FastAPI ASR Service localhost:8000
/transcribe (Whisper base) /extract (spaCy + Ollama) /transcribe_and_extract
OpenEMR (Docker · localhost:80)
Encounter form textarea[name="reason"] Reason for Visit field
⟷
⟷
POST audio / JSON transcript
DOM injection (no HTTP)
Key Decisions: Local Whisper — privacy + offline · FastAPI — browser-callable, model-swappable · Extension over PHP edits — no OpenEMR source changes · CORS middleware — extension ↔ API · Confirm-before-fill — patient safety UX
⚠ All audio and text stays on the provider's machine — no network egress

## Slide 8
AT1 — Field Detection
Acceptance Test 1 of 5
What we show:
1. Open OpenEMR encounter page in Chrome with extension loaded
2. Observe: extension panel appears, attached to the right of the page
3. Observe: 'Reason for Visit' textarea is highlighted in green
4. Navigate to login page — panel does NOT appear
PASS criteria
✓ Panel appears only on encounter / new-patient pages
✓ Correct field (textarea[name="reason"]) is identified and highlighted
✓ Panel stays hidden on the login page

## Slide 9
AT2 — Transcript Preview & Edit
Acceptance Test 2 of 5
What we show:
1. Click 'Use demo text' in the extension panel
2. Observe: 'Patient reports headache and mild fever for two days.' appears
3. Edit the preview text directly in the panel
4. Observe: edits persist in the preview before any form interaction
PASS criteria
✓ Demo transcript loads instantly into the preview textarea
✓ Preview text is fully editable by the clinician
✓ No text has been written to the OpenEMR form yet

## Slide 10
AT3 — Confirm-Before-Fill Safeguard
Acceptance Test 3 of 5
What we show:
1. With a transcript loaded in the preview, click 'Insert into form'
2. Observe: browser confirmation dialog appears
3. Dialog shows the proposed text AND the target field name
4. Click Cancel — observe that the OpenEMR form is unchanged
PASS criteria
✓ Confirmation dialog fires before any DOM write
✓ Proposed text and field name are visible to the clinician
✓ Cancelling leaves the OpenEMR form exactly as it was

## Slide 11
AT4 — Successful Field Insertion
Acceptance Test 4 of 5
What we show:
1. With transcript in preview, click 'Insert into form', then confirm
2. Observe: transcript text appears in the 'Reason for Visit' textarea
3. Verify: no other form fields (date, checkboxes, selects) were modified
4. Optionally: save the encounter and verify the text persists
PASS criteria
✓ Field value matches transcript exactly
✓ No other OpenEMR fields are modified
✓ Text triggers React-compatible input/change/blur events

## Slide 12
AT5 — Real Microphone Transcription
Acceptance Test 5 of 5
What we show:
1. Click 'Start mic' — browser prompts for microphone permission
2. Speak: 'Patient presents with shortness of breath and chest tightness'
3. Click 'Stop' — observe recording pulse stops, status shows 'Transcribing'
4. Observe: Whisper transcript appears in preview panel within ~2 seconds
5. (Optional) Show terminal: POST /transcribe_and_extract → NLP entities
PASS criteria
✓ Transcript matches spoken phrase (WER < 10% for clear speech)
✓ Text appears in the preview within 2 seconds of pressing Stop
✓ NLP /extract correctly identifies chief_complaint entity

## Slide 13
Special Accomplishments
End-to-End MVP
Voice → Whisper → NLP → OpenEMR field insertion — fully working in 3 iterations
Dual NLP Architecture
spaCy fast path (<100ms) + Ollama LLM option with graceful fallback; runs on any hardware
Zero OpenEMR Source Changes
Extension attaches non-invasively — no PHP edits, no fork, survives OpenEMR updates
Stakeholder-Validated Safety UX
Confirm-before-fill proposed by the team, then explicitly validated by Nirav Merchant
Docker-Based Local Dev
Full OpenEMR + FastAPI environment reproducible on any team member's machine
CORS-Enabled API
FastAPI service correctly handles cross-origin requests from Chrome extension

## Slide 14
Challenges
Medical Terminology Accuracy
Whisper base model struggles with drug names and clinical procedures — visibly lower accuracy on jargon. Model evaluation (MedASR / MedWhisper) is planned.
Scoping Under Pressure
Team faced serious personal circumstances mid-project. Deliberately narrowed MVP to one field (Reason for Visit) to deliver something real and demo-able.
Three-Part Integration
Chrome extension + local FastAPI + Dockerized OpenEMR must all run simultaneously. Mid-sprint integration checkpoints (Wednesdays) caught a critical API response mismatch early.
No Automated Test Suite Yet
All testing was manual end-to-end. Automated acceptance tests tied to WER / accuracy / latency criteria are the first deliverable in the next sprint.

## Slide 15
Final Takeaways
Local AI in Healthcare Works
The full pipeline — microphone → Whisper → NLP → EHR field — runs entirely on the provider's machine. No cloud, no subscription, HIPAA-aligned by design.
Scope Aggressively, Ship Something Real
Narrowing to a single customer-validated field (Reason for Visit) delivered a working demo instead of an incomplete multi-field prototype.
Stakeholder Feedback Drives Design
Nirav Merchant's patient-safety concern produced the most impactful design decision in the project (confirm-before-fill). Engage stakeholders early and often.
Foundation for Expansion
More fields, MedASR/MedWhisper models, WebRTC noise suppression, SOAP notes, and HIPAA documentation are natural next steps from a solid working base.
Thank you. Questions?